## Slide 1: 2024 Forest Practices Audit
Hawk Stone
Water Quality Scientist
Idaho DEQ
Notes: Where is NIPF better than the rest? Variances. Maintenance debris. SPZ harvest. Maintaining skid trails. Siting skid trails in stable locations.
Worse? Installing culverts and ditches (tend to skip them). Minimizing fill erosion. Maintaining bridges and culverts. Repairing erosion sources to streams. Using equipment and piling slash in the SPZ.

## Slide 2: 2020 Memorandum of Understanding

## Slide 3
58 Audit Sites
Site Requirements
Harvested in last 2 years
Contain a fish-bearing stream
At least 5 acres
All ownerships
Notes: Divided between ownerships
58 sites: 19 industrial private, 14 state, 14 federal, 11 non-industrial private
Stratified Randomly selected – spread across ownership, state and IDL admin area
Not surprise

## Slide 4: Website

## Slide 5: Meet the new audit team

## Slide 6: Audit Process
Notes: Walk entire sale, especially stream crossings, drainage pipes and new roads.
Compare every situation to as many of the Rules as possible: 139 possible rules.
Total of Idaho Forest Practices Act rules: 2250 observations

## Slide 7: 2024 Improvements
Further refined field forms
Incorporated new rules
Shade recovery study
More efficient

## Slide 8: Overall Compliance
Chart: 
| 1984 | 1988 | 1992 | 1996 | 2000 | 2004 | 2008 | 2012 | 2016 | 2020 | 2024
Average | 81.75 | 93 | 93 | 96.5 | 95.75 | 97.75 | 96 | 98.25 | 96.25 | 96 | 94.5
Out of 2,250 observations,
2,133 were in compliance
95%
?

## Slide 9: Compliance – by Ownership
Chart: 
| State | Private Non-Industrial | Private Industrial | Federal | AVERAGE
 | 0.91906 | 0.93111 | 0.96429 | 0.97028 | 0.948
AVERAGE COMPLIANCE

## Slide 10: Compliance Through the Years
Chart: 
| 1984 | 1988 | 1992 | 1996 | 2000 | 2004 | 2008 | 2012 | 2016 | 2020 | 2024
Average | 81.75 | 93 | 93 | 96.5 | 95.75 | 97.75 | 96 | 98.25 | 96.25 | 96 | 94.5
Federal | 96 | 94 | 93 | 100 | 98 | 100 | 98 | 99 | 97 | 96 | 97
Private Industrial | 82 | 95 | 96 | 98 | 94 | 99 | 96 | 99 | 97 | 97 | 96
Private Non-Industrial | 82 | 86 | 94 | 95 | 95 | 93 | 91 | 96 | 95 | 96 | 93
State of Idaho | 67 | 97 | 89 | 93 | 96 | 99 | 99 | 99 | 96 | 95 | 92

## Slide 11: Compliance Example
Chart: Instances
| 030 03d Erosion minimized during downhill cable yarding? | 030 04a Landings and trails in stable areas outside of SPZ? | 030 04a Skid and fire trails located to minimize sidecasting? | 030 04b Size of landings appropriate? | 030 04c No loose stumps nor excessive slash in landing filler? | 030 04c Sidecasted landings properly stabilized?
Complied | 2 | 35 | 36 | 36 | 6 | 5
Did Not Comply | 0 | 7 | 2 | 0 | 1 | 1

## Slide 12: Number of Violations per Site
Chart: Number of Violations at an Audit Site
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
 | 25 | 5 | 11 | 8 | 3 | 2 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0
 | 0.43103 | 0.086207 | 0.18966 | 0.13793 | 0.051724 | 0.034483 | 0 | 0.017241 | 0 | 0 | 0 | 0.017241 | 0.017241 | 0 | 0.017241 | 0

## Slide 13: What were the Most Common/Serious Problems?
Bare dirt in the Stream Protection Zone from maintenance and construction (20% of violations)
Slash piles in the Stream Protection Zone
Culvert pipes too short and road fills unstable
Water-truck screens missing/too large
020.02(c)(iii): Water diversion intakes … must be screened with a maximum screen mesh size [of]… 3/32 inch [Class I streams]
Short culvert pipes & unstable fills
030.07f(ii): No mechanical piling of slash… is allowed in an SPZ
040.03(b): Clear all debris generated during construction… which potentially interferes with … water quality.
040.04(a): Place all debris… associated with road maintenance in a manner to prevent [its] entry into streams.

## Slide 14: Comparison to 2020 Audit
We didn’t have to wear N-95 masks.
Grease tubes and oil buckets are still mostly being cleaned up (74% compliance in 2016, 95% in 2020, 88% this year).
More severe Stream Protection Zone violations –mostly from short culverts
Fish passage rules and shade rules much better this year.
Fewer ‘perfect’ sites

## Slide 15
Perfectly decommissioned road

## Slide 16
Nice temporary crossing

## Slide 17
Clear instructions

## Slide 18: Recommendations
IDL inspectors should pay extra attention to unstable bare dirt located near a stream.
Rule variances must be more carefully justified, and inspected. They should address temperature as well as sediment impacts.
Rule change: add requirement to stabilize erodible fills near the stream as soon as practical (instead of seasonally).
Rule change: require culvert pipes to be long enough to prevent erosion of the fill.
Rule change: explicitly prohibit large slash piles next to streams.

## Slide 19
11 Weeks
27 Shade Sites
58 Audit Sites
119 Guests
2,250 Rules
20,000 Miles

## Slide 21
Questions?
www.deq.idaho.gov/forestry
www.idl.idaho.gov/forest-practices-act